Licensed under the TAPR Open Hardware License (www.tapr.org/OHL). A copy of the license is included. See file: LICENSE.TXT

GNU General Public License

This program is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version.

This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.

You should have received a copy of the GNU General Public License along with this program. If not, see <http://www.gnu.org/licenses/>. A copy of the license is included See file: GPL.TXT

Innovators:	Liselotte Scheu dba Scheus Rainbow Army email: kappa@dekka.com
17600 S. Pacific HWY #20
Marylhurst, OR 97036-0020 usa
Place of performance:	place of business
Employer status:	self-employed (SB)
Contribution:	commercial, material, motivational support

Benjamin Brink	c/o Scheus Rainbow Army
Origin:	self
Innovator representative:	self
New technology representative:	self

Abstract

This hardware design is a solid-state synchrotron that multiplies an input voltage with each resonating induction cycle, and is capable of emitting electromagnetic waves at specific sets of frequencies and may emit plasma from a cascade of alternating EM flux. Speculatively, this device has the potential to meet multiple, fundamental target technology design challenges. 1. It may make spacecraft ion drives economical by markedly increasing efficiency of plasma generation. 2. It may be used in portable, water-fueled rocket engines to propel airliners that are vulnerable to volcanic ash in flight. 3. It may be used in high voltage transmission line technology as part of voltage multipliers, power recovery units, and a power terminal transfer device. 4. It may be used for high performance, ultra high frequency motors and centrifuges. 5. It may be used to facilitate transportation using levitation techniques. 6. It may provide a significant component as an alternate to fluorescent lighting starter and ballast configurations that contain mercury that is hazardous to the environment (See Eel Trick Wire project). 7. A linear variant of the main ring may provide a more reliable, efficient conversion of high-voltage electrical power at power conversion stations for electrical power transmission (See Eel Trick Wire project).

Table of Contents

Background (of invention)
Section I. Problem
Section II. Technically complete description of innovation
II.A. Purpose and description of innovation
II.B. Identification of component parts or steps, and explanation of mode of operation of innovation (with sketches)
II.C. Functional operation
II.D. Alternate embodiments of the innovation
II.E. Supportive theory
II.F. Engineering specifications
II.G. Peripheral equipment.
II.H. Maintenance, reliability, safety factors.
Section III.
III.A. Novel or unique features.
III.B. Advantages of innovation.
III.C. Development or new conceptual problems.
III.D. Test data and source of error.
III.E. Analysis of capabilities.
Section IV. Potential commercial applications and points of contact
Section V. Other
V.A. Additional documentation:
V.B. Degree of technology significance:
V.C. State of development:
Section VI. Patent status
VI. Signatures of innovator(s), witnesses.

Background

This device was initially conceived in 1981 as a boundary test to reconcile observations of electromagnetic phenomenon with electromagnetic theory in physics versus electronics. In particular, the test compared induction performance between a single-layer coil of round-wire and a loop antenna array of same dimensions of coil. The coil wire wraps around a cylinder with an insulating gap thereby forming a helix. The loop array consists of round-wire loops with a common axis of symmetry, dimensions and gap spacing of the wire coil, except where loops are coupled by a straight round-wire on the inside of each loop.

Section I. Problem

What are the limits of collecting electromagnetic energy into a standing wave of ever increasing energy density for purposes of energy utility by using common materials of solid-state electronics?

Section II. Technically complete description of innovation

II.A. Purpose and description of innovation

This solution is a solid-state, high-Q resonator that steps up voltage (and decreases current) with each set of inductance cycles using a minimum of common electric materials and shapes in an innovative configuration. For each interval of time greater than one resonant cycle, the capacity to hold more energy increases because the oscillating electric current decreases as the voltage (electric potential) increases. The voltage increase is a process somewhat similar to how an automobile ignition coil induces a higher voltage even though a pole is shared between the primary and secondary induction coil. The flexible design has multiple means of feeding electromagnetic energy to the apparatus. The structure of the apparatus provides predictable fixed, pre-tuned frequencies of operation.

II.B. Identification of component parts or steps, and explanation of mode of operation of innovation (with sketches)

II.B.1. Main current ring

The main ring consists of a uniform circular torus of electrically conductive material. See Figure 1. The torus is defined by a circle of radius r1 rotated about and coplanar to an axis line of symmetry (z axis) at a distance r2 from the center of the circle p1 to the point p2 on the axis. c1 is the circumference of the circle of radius r1 with center p1. c2 is the path of the center of the circle defining the torus. The torus may be represented by a physical tube or rod.

variables:	r1	radius of cross-section of torus tube “main ring”
c1	circumference of circle with radius r1, also refers to circles of same.
p1	center point of circle with radius r1
a1	area of the cross-section of the torus tube
r2	radius from axis to center of circular cross-section of torus tube
c2	circumference of circle with radius r2
p2	center point of circle with radius r2
û(r2)	an arbitrary unit length radial direction of r2 (a versor)

II.B.2. Secondary rings

Secondary rings consist of a set of identical torus rings of electrically conductive material connected to the main current ring at the surface closest to the axis of symmetry z. See Figure 1 for references. Secondary rings are oriented coplanar to circles c1 in Figure 1 and strategically connected to the main current ring at the point closest to axis z in Figure 1. Secondary rings may be represented by tube or rod.

Figure 2 shows a slice of a secondary ring around a cross-section of the main ring. References are consistent with main current ring variables. Other variables:

variables:
r3	radius from axis to center of circular cross-section of a torus tube
c3	circumference of a circle with radius r3
p3	center point of a circle with radius r3
r4	radius of cross-section of a torus tube ie secondary ring
c4	circumference of a circle with radius r4, also refers to circles of same.
p4	center point of a circle with radius r4
a4	area of cross-section of a secondary ring
k	number of secondary rings
k2	a ratio of (a4 * k) / a1

Figure 3 shows a partial diagram of the apparatus from a plane above and perpendicular to Z-axis, for an example k = 24

2(r4)	the diameter of a secondary ring ie twice the radius r4.
r5	radius from z axis of symmetry to center of optional induction conductor
c5	circumference of an optional induction conductor

II.C Functional operation

Multiple processes of an operation cycle result in periodic electromagnetic self and mutual induction. Circuit performance includes complex capacitance (conductor) charging and discharge, and mutual and self induction. Conventionally identifiable processes include: main ring as antenna, secondary rings as antenna array, main to secondary charge coupling, secondary to main charge coupling. There are a variety of ways to use this apparatus in a circuit. Only the simplest are discussed. The apparatus primarily functions to generate complementary resonating cycles resulting in higher voltage and lower current that would be expected of a high-Q transformer where the primary leads are connected to the secondary leads ie a high frequency LC circuit.

II.C.1 Mutual-induction of main ring by electromagnetic pulse or sporadic ion stream (charge current).

For example, consider a transient electromagnetic pulse such as the trailing edge of a voltage spike resulting from opening a closed DC circuit. A pulse following a straight cylindrical conductor along the Z-axis of symmetry may induce a current in the apparatus at the main ring as the charge and magnetic field originating from the Z-axis changes. A quickly changing current has high-frequency AC properties. When high-frequency properties occur, the current density of the Z-axis conductor is not uniform, but tends to move along the surface due to the “skin effect” and law of distribution of charges. Frederick W. Grover states in his book “Inductance Calculations: Working Formulas and Tables” published in 1946 by D. Van Nostrand Company, “..If the frequency is so high that the current may be considered as essentially confined to the surface of the conductors, then an electromagnetic wave is propagated along the wires with the velocity of light.. (page 262). ” In the presence of an electromagnetic field, the electromagnetic wave (charged particles) will follow a helical path or vortex thereby emitting electromagnetic radiation at a frequency near to the wavelength of the conductor's circumference, thereby providing an additional opportunity for electromagnetic energy to be transferred to the apparatus.

II.C.2 Mutual-induction of secondary rings by electromagnetic pulse or sporadic ion stream (charge current).

For example, consider a transient electromagnetic pulse such as the trailing edge of a voltage spike resulting from opening a closed DC circuit. A pulse following a straight cylindrical conductor along the Z-axis of symmetry may induce a current as mutual induction at the secondary rings as the magnetic field originating from the Z-axis changes.

II.C.3 Charge distribution dynamics

With each dynamic, any charge variance between any part of the apparatus will seek equilibrium similar to a capacitor's plate. This process helps to maximize the work of any inductive signal by providing charge where convention might indicate no charge differential exists.

II.C.4 A more detailed function of apparatus

This section focuses on describing the nature of the resonant cycle in an ideal environment. A portion of the energy is lost to heat from impedance, hysteresis and eddy currents.

The apparatus' operates in high-Q resonance between two induction cycles. The main operating principles are:

Self and mutual inductance of round-wire (or current sheet) in go-and-return circuits,
Lenz's law of counter created current from inductance, and
Coulomb's law of electrostatic charge distribution.

If using math to predict operation, approach the system using discrete charge dynamics and first principles of physics to reduce complexity.

If tuned to resonate with repeated input, voltage continues increasing while current decreases thereby increasing capacity to handle more charge. The cascade of increasing voltage terminates at the apparatus' maximum voltage limit due to corona discharge and breakdown. The additive nature of successive cascading inductions can collect sufficient energy over a duration to produce forces capable of higher capacity work.

Output as work may include output of electromagnetic radiation that breaks chemical compounds such as water into hydrogen and oxygen and manipulating ions via charge dynamics as part of an ion drive, electric discharges and organized electromagnetic emissions and forces used in many innovative ways as suggested in the abstract above.

For example, tuned to emit critical electromagnetic absorption frequencies, the apparatus could potentially heat water to water-vapor state and subsequently ionize water-vapor to decomposition, where high-voltage breakdown ignites the oxygen and hydrogen mixture thereby creating an alternative to jet propulsion et cetera.

Note: Although a single apparatus configuration is described with reference to alternate embodiments, experts will recognize that changes may be made in form and detail without departing from the spirit and scope of the invention.

II.D. Alternate embodiments of the innovation

The rings may also be made of varying conductors, such as outer layers of metal and an inner, electrically low resistant liquid and/or gas conductor. In accordance with supporting theory (section II.E), the function of the apparatus may be augmented when the layers of varying material are symmetric to the circular axis c2 in Figure 1, and if applied to the secondary rings, also symmetric to the circular axis c3 in Figure 2.

II.E. Supportive theory

This apparatus is designed to leverage subtle effects of electricity and Lenz's law in an innovative way. The subtle effects include 1. that a current in a collapsing magnetic field (such as from self-inductance of a current in a round wire) tends to travel in a spiral or vortex due to Lenz's law, 2. that power losses from heat are reduced as voltage increases, 3. that eddy currents, including the “skin effect” become more significant as AC current's frequency increases, 4. that skin effect, where electron charge density increases toward a wire's surface, increases with increasing frequency, charge, or voltage (electric potential).

II.E.1. Charged particles spiral in collapsing or increasing DC current

Collapsing or increasing DC current may form a spiraling vortex of charged particles due to Lenz's law as it crosses and follows the path of a conductor, and that the boundary and other conditions of a conductor determines the characteristics of the vortex, where current density tends to be higher near a conductor's surface. For a DC current in a wire, the current spirals mostly near the surface boundary of cylindrical wire. Electromagnetic interference (EMI) is the result of emission from a cross-section of the vortex, where the frequency of EMI tends to be proportional to the wavelength of the circumference of a circular cross-section of the wire.

Consistent observations include: Correlations between VLF wavelength observations of lightning EMI and the physical evidence of lightning bolt cross-section circumferences (calculated from widths of direct strike damage); and correlation between atmospheric "chorus" phenomenon starting at circa 600Hz and a larger inner Van Allen belt cross-sectional circumference (circa maximum 1/4 Earth radius times pi) with chorus frequency increasing suggesting a disintegrating ie narrowing of the belt.

There may also possibly be correlation to predicting EMI in electrical circuit design: Cavicchi, T. J. "Multiple reactions in inductors," Education, IEEE Transactions on, vol. 40, No. 1, pp.78,88 Feb. 1997; and a hypothesis that applying Lenz's law recursively could explain a physical cause of electron spin and suggest a spiral component of electron motion consistent with Randell L. Mills' mathematical representation of the electron as a spinning flat disc in his Grand Unified Theory of Classical Physics.

This is a hypothesis in progress. Access to a well equipped physics-electronics lab or HV-DC power transmission field experience could help quantify or determine more general patterns and its limitations.

II.E.2. Increasingly high voltages reduces power losses from heat

Heat losses are attributable to electrical resistance from current. By increasing voltage and subsequently decreasing current, resistive heating decreases.

Joule's first law states that for a given quantity of electrical power and conductor size, power loss as heat in wires is not dependent on voltage, but is proportional to the square of the current. Doubling the voltage results in the same power at half the current, subsequently losses from resistive heat are reduced to 25% of previous amount.

II.E.3. Eddy currents increase as AC frequency increases

This apparatus is designed to resonate at the frequency of its collapsing magnetic field, which causes a rebounding field to grow. Therefore, the effects of eddy currents may be maximized, and the apparatus reach near a maximum high-Q resonance.

II.F. Engineering specifications

Refer to Figures 1 to 3 for visual representation of definitions.

Dimensions and measurements

r2 is larger than r1
r2 is circa an integer multiple of r1
A4 x k ≥ A1
c3 = c1 x j1, where j1 is within the range of a positive integer ∓ r4 and c3 > 1
c1, c2, and c3 are circa integer multiples of the length of c4
c5 is an integer multiple of c4

Materials

Rings may be solid metal conductor of low resistivity, such as low oxygen copper or silver. Optionally rings may consist of layered materials symmetric to c3 or c2. Optional layered material may be another form of conductive material, such as a liquid.

An inductor conductor should be cylindrical and symmetric to the z-axis.

Manufacturing and assembly

Main ring is connected to secondary rings in a way that minimizes resistance and corona discharge.

Secondary rings' projected planes are oriented at near right angle to main ring's projected plane.

Secondary rings may be equally spaced along the main ring, or grouped and the groupings spaced equally along the main ring.

II.G. Peripheral equipment

Depending on application, a signal generator may be required to connect to an inductor conductor for energy input; Or, an electromagnet positioned at p2 with the magnetic pole oriented along the z axis of symmetry.

II.H. Maintenance, reliability, safety factors.

Appropriate safety precautions should be used when working with high frequencies, high voltages and/or non-ionizing radiation.

Early experiments suggest the apparatus material is susceptible to accelerated oxidation and/or corrosion. Long-term performance reliability of an apparatus may depend on identifying new materials with properties resilient to degrading; or manufacturing apparatuses with predictable failure patterns.

Section III. Innovation parameters

III.A. Novel or unique features.

Resonance is driven by a complex of capacitance and antenna dynamics.

III.B. Advantages of innovation.

An ion drive may require less energy for equivalent thrust.

Airliners may be able to fly regardless of the presence of volcanic ash.

High voltage power transmission lines may have less losses or power conversion stations built less expensively.

Ultra high frequency motors or centrifuges might operate with greater efficiency.

Levitation may become a practical mode of transport in some situations.

Fluorescent lighting starters may not need to include hazardous and expensive materials such as mercury.

III.C. Development or new conceptual problems.

By understanding boundary charge flow, faster and more effective electrical components may be designed with predictable EMI and subsequently less EMI issues.

III.D. Test data and source of error

An apparatus was built with values k=94, k2=1.7, r1= 2.38mm, r2=22.2mm, r3=3.3mm, r4=0.322mm with an induction rod radius of 2.38mm. Apparatus material consisted of low oxygen copper. A flash at a malformed secondary ring was captured via a DSLR using a 3 second f/2.5 exposure, consistent with corona discharge of Nitrogen in air. See file: PRIOR-ART-PROOF-OF-CONCEPT.odt for details.

III.E. Analysis of capabilities.

An untuned apparatus appears to work under poor conditions, suggesting this apparatus has potential in achieving design goals.

Section IV. Potential commercial applications and points of contact.

Contact innovator.

Section V. Other

V.A. Additional documentation: none.
V.B. Degree of technology significance: potentially disruptive
V.C. State of development: early design and prototyping

Section VI. Patent status

Released under the TAPR Open Hardware License version 1.0

See file: PRIOR-ART-PROOF-OF-CONCEPT.odt for prior art details.

VII. Signatures of innovator(s), witnesses.

Benjamin Brink	20 May 2013
innovator

Liselotte Scheu	20 May 2013
witness

Eric Scheu	20 May 2013
witness